## Slide 1: Applying Finite Volume Method to Solve the 2D Compressible Inviscid Navier-Stokes Equations
MA448 Final Project Part II
Spring 2022 - Khanal
By: Zach Eckley

## Slide 2: Motivation
Began as a method to solve internal ballistics for solid rocket motors
Began with a simpler FVM application
Hit snags with adaptive mesh
  Port shape changes over time
  Had trouble keeping same mesh connections
  Didn’t find a working method until the start of the fall semester
Got FVM to work for water and then for air
Haven’t touched the project much since then

## Slide 3: Motivation
Began as a method to solve internal ballistics for solid rocket motors
Began with a simpler FVM application
Hit snags with adaptive mesh
  Port shape changes over time
  Had trouble keeping same mesh connections
  Didn’t find a working method until the start of the fall semester
Got FVM to work for water and then for air
Haven’t touched the project much since then

## Slide 4: Topics
Mesh creation
  Unstructured Mesh
  Utilized PDE toolbox in Matlab
  Variable cell density

## Slide 5: Topics
Mesh creation
Finite Volume Method

## Slide 6: Topics
Mesh creation
Finite Volume Method
Setting up the equations
  First order Finite Volume Method
  Navier-Stokes
  Compressible
  Inviscid

## Slide 7: Topics
Mesh creation
Finite Volume Method
Setting up the equations
Applying boundary conditions
  Dirichlet for inlet
  Neumann for outlet
  Neumann for wall

## Slide 8: Topics
Mesh creation
Finite Volume Method
Setting up the equations
Applying boundary conditions
Solution method used
  Equations set up in column vector
  ODE45 solved the system
  Chosen because it’s a MATLAB function and its adaptive

## Slide 9: Topics
Mesh creation
Finite Volume Method
Setting up the equations
Applying boundary conditions
Solution method used
Displaying Results

## Slide 10: Delaunay Triangulation
Part 1
Creates pde model
Creates shape from x and y
Creates “pet” arrays
Uses p and t to make geometry
Part 2
Max and min cell size are chosen
Mesh is created based on cell size and geometry created previously

## Slide 18: Mesh Information
Level | Node # | Cell # | Avg q | Max q | Min q | q≥0.95
1 | 129 | 208 | 0.982 | 1.000 | 0.793 | 90.685%
2 | 273 | 470 | 0.990 | 1.000 | 0.796 | 94.681%
3 | 709 | 1294 | 0.994 | 1.000 | 0.922 | 98.223%
4 | 1549 | 2912 | 0.995 | 1.000 | 0.894 | 97.218%
5 | 3019 | 5776 | 0.996 | 1.000 | 0.887 | 98.996%
6 | 8203 | 15972 | 0.997 | 1.000 | 0.912 | 99.192%
7 | 25879 | 50980 | 0.998 | 1.000 | 0.895 | 99.310%

## Slide 20: Delaunay Triangulation
P – points/nodes in the mesh. Lists x and y coordinates of each node [2xN]
E – Elements/cells in the mesh. Lists the three nodes that create it in terms of their index in P. [3xE]
T – Connectivity list. Includes which nodes are connected to create a cell

## Slide 21: meshInfo function
Cell areas are found
Side lengths are found
Side normals are found
Find cell connectivity by finding cells that share 2 points

## Slide 22: Finite Volume Method
Finite volume looks at the movement of properties throughout the cells rather than specific values.
2D cases require analysis of the flux in X and Y
3D cases require additional analysis of flux in Z
Over many times steps the flux in and out of the cell will balance to achieve steady state
Allows for the analysis of both structured and unstructured meshes

## Slide 23: Equations
Inviscid Compressible Navier –Stokes | 
Continuity | 
X Momentum | 
Y Momentum | 
Energy | 
Inviscid Compressible Navier –Stokes | 
Continuity | 
X Momentum | 
Y Momentum | 
Energy | 
Cj
Ci
Mass flux in x dir.
X momentum flux in x dir.
Y momentum flux in x dir.
Energy flux in x dir.
Mass flux in y dir.
X momentum flux in y dir.
Y momentum flux in y dir.
Energy flux in y dir.
Finite Volume Scheme

## Slide 24
Fx out
Fy out
Fx in
Fy in

## Slide 25: Numerical Dissipation
Value added to the flux terms at the end to prevent instability
Compressible equations can cause shocks to form in the solution.
Shocks act as discontinuities and can cause problems
By utilizing wave speed of the cell and neighboring cells a discontinuity can be created without causing problems in the solution.
Modifies the final equation to the following
Without this modification the solution can fail if shocks occur

## Slide 26: Boundary Conditions
Outlets
Labeled as -1
“Ghost node” approach
Imaginary cell is “created” on opposite side.
Allows steady flux out of the cell based on the conditions of cell at that time.
Neumann condition at outlets allowing free flow of quantities
Inlets
Labeled as -2
Flux is defined before solution begins
Flux is equal to whatever the user set it to
Dirichlet condition at inlet sides with user defined flux values.
Walls
Labeled as -3
Flux outwards is 0 because the wall prevents flux
With heat transfer energy flux could be possible
Mass flux should remain 0 unless ablation occurs at high speeds
Neumann condition at wall sides with first derivative equal to 0

## Slide 27: Setting up RK4 (ode45)
Fi is a matrix of the first order time derivatives of the conditions of the cell
ddtAir function uses the connectivity, the normals, and the areas of each cell to calculate the first order derivatives using the finite volume method.
Those first order derivatives are then set up in a column vector and solved in ode45

## Slide 28
Set up Mesh
Determine Boundaries
Define and create IC
Collect Mesh info
Organize Inputs
Calculate y flux
Calculate x flux
Create array of neighboring flux for each cell
Calculate wave speed
Combine Flux and Numerical dissipation
ode45 solves dwdt vector
Organize flux into dwdt vector
End of time span?
Display/Update Results
No
Yes

## Slide 44: References
[1] Flux vector splitting scheme - TIFR centre for applicable ... Flux Vector Splitting Schemes. (n.d.). Retrieved April 22, 2022, from http://math.tifrbng.res.in/~praveen/notes/acfd2013/fvs.pdf
[2] Finite volume method on unstructured grids. (n.d.). Retrieved April 22, 2022, from http://math.tifrbng.res.in/~praveen/notes/acfd2013/fvm.pdf
[3] Anderson, J. D. (1982). Modern compressible flow. McGraw-Hill.
[4] A positivity preserving ﬁnite element–ﬁnite volume solver ... (n.d.). Retrieved April 22, 2022, from https://people.math.carleton.ca/~elorin/paper_spalart.pdf
[5] Gueyffier, D., Onera, Roux, F. X., Fabignon, Y., Chaineray, G., Lupoglazoff, N., Vuillot, F., Hijlkema, J., Alauzet, F., Institut National de Recherche en Informatique et en Automatique Paris-Rocquencourt, M., B., H., R., L., K. A. and G., A, K., A., W. M., D., D. F. and R., R., A. S. and A., S., S. J., E., C., … J., D. (2015, August 11). Accurate computation of grain burning coupled with flow simulation in Rocket Chamber. Journal of Propulsion and Power. Retrieved April 22, 2022, from https://arc.aiaa.org/doi/10.2514/1.B35736
[6] Chang, C.-L. (2006). Time-accurate, unstructured-mesh Navier-Stokes ... Retrieved April 22, 2022, from https://ntrs.nasa.gov/api/citations/20060027797/downloads/20060027797.pdf?attachment=true
[7] Hirsch, C. (2007). Numerical computation of internal and external flows (2nd ed.). Elsevier/Butterworth-Heinemann.